## Slide 1
Design and Implementation of 8-Bit ALU Using VHDL
Course: VLSI Technology: VHDL Simulation Tool: ModelSim Implementation Tool: Xilinx Vivado Target FPGA: PINE S7 (Spartan-7 XC7S15FTGB196-1) Presented by: Team VLSI Innovators Date: 27/02/2026

## Slide 2
Introduction to ALU
ALU = Arithmetic Logic Unit
Core component of CPU
Performs arithmetic and logical operations
Operates on binary data
Controlled using selection signals
Produces result output

## Slide 3
Project Objective
Aim of the Project
Why 8-bit?
Simple and efficient design
Suitable for learning processor fundamentals
Moderate hardware complexity
Design 8-bit ALU using VHDL
Implement 16 operations using 4-bit select line
Perform multiplication (lower 8 bits only)
Implement division with divide-by-zero protection
Simulate using ModelSim
Implement on PINE S7 FPGA

## Slide 4
Functional Operations (16 Operations)
Arithmetic Operations
1.
2.
3.
4.
5.
6
Logical Operations
AND
OR
XOR
XNOR
NAND
NOR
NOT A
NOT B
Shift Operations
Logical Left Shift
Logical Right Shift
(Controlled using 4-bit select input S3 S2 S1 S0)
ADD (A + B)
SUB (A − B)
MUL (Lower 8 bits only)
DIV (With zero check)
INC (A + 1)
DEC (A − 1)

## Slide 5
Block Diagram Description
Main Components of the ALU
Two 8-bit Inputs (A and B)
4-bit Selection Input
Arithmetic Unit
Logic Unit
Shifter Unit
16-to-1 Multiplexer
Status Flag Generator
Output
8-bit Result
Flags:
  Carry (C)
  Zero (Z)
  Sign (S)
  Overflow (V)

## Slide 6
Used IEEE.STD_LOGIC_1164.ALL
Used IEEE.NUMERIC_STD.ALL
Inputs converted to unsigned for arithmetic
Case statement used for operation selection
Combinational process block
Result converted back to STD_LOGIC_VECTOR
Industry-standard coding practice followed.
VHDL Design Approach
Design Methodology

## Slide 7
Simulation and Results
Simulated in ModelSim
All 16 operations tested
Example: A = 00001111 (15) B = 00111000 (56) MUL → 840 Output = 01001000
Division by zero → Output = 00000000
Waveforms confirmed correct functionality

## Slide 8
SIMULATION AND RESULT

## Slide 9: SIMULATION AND RESULT

## Slide 10: FPGA Hardware Implementation
Target Board: PINE S7 Spartan-7
Input Mapping:
SLIDE_SW[7:0] → Input A
SLIDE_SW[15:8] → Input B
Push Buttons → SEL
Output Mapping:
LED[7:0] → ALU Output
Constraint file (.xdc) used for pin mapping.

## Slide 11: Key Features of Our Design
Fully combinational ALU
16 functional operations
Multiplication truncation handled correctly
Divide-by-zero protection implemented
Synthesizable design
Scalable to 16-bit and 32-bit systems

## Slide 12: Synthesized design

## Slide 13
Conclusion and Future Scope
Conclusion
Successfully designed 8-bit ALU
Implemented 16 operations
Verified using simulation
Implemented on FPGA hardware
Future Improvements
Add carry, zero and overflow flags
Extend to 32 bit ALU
Integrate in simple processor

## Slide 14
THANK YOU

## Slide 15
ANY QUESTIONS ???